## Slide 1
A VISION BY ALI ALENEZI · KUWAIT CITY
Smart Souq Al-Mubarakiya
This is my dream for Al-Mubarakiya, and I wanted to share it with everyone: that the souq stays as we know and love it, with its soul and its history, and becomes safer through smart technology that works in silence.
Sensors nobody notices, an edge that keeps the fire alarm working when the cloud does not, a digital twin built on the map, and trust zones around all of it.
A personal vision, shared to read and discuss. · mubarakiya.3li.info
This work is part of an educational experience. The ideas are owned by Ali AlEnezi. The entities mentioned, Kuwait Municipality, the Ministry of Interior, Kuwait Fire Force, NCCAL, CITRA, the Ministry of Electricity and Water, the Ministry of Commerce, the merchants, and SANS, are mentioned only to elaborate on the ideas and have no real link or connection to this work. SANS is named only as a suggestion for training, and none of its copyrighted material is used here. © 2026 Ali AlEnezi. All rights reserved.
Ali AlEnezi · Site@hotmail.com · 3li.info
Notes: Open with the dream. Make clear this is a personal vision, shared to read.

## Slide 2
01 // WHY THIS SOUQ
Two centuries old, pedestrian, dense, and loved
Smart Souq Al-Mubarakiya · a vision by Ali AlEnezi
Heritage
Nothing drilled into historic facades. Sensors on lamp posts, awnings, and municipal fixtures. NCCAL signs off first.
Climate
50 C summers and dust storms. Every device rated 60 C or better and IP65 or better, solar where wiring is forbidden.
Life safety first
Narrow alleys, wooden roofs, dense restaurants, peak crowds. Fire and crowd safety are use case number one.
Many owners
Municipality, MOI, Kuwait Fire Force, NCCAL, CITRA, MEW, Commerce, and the merchants. Governance is half the project.
Privacy
Count people, never identify them. No facial recognition, anonymized counting at the edge, signage in the souq.
Ali AlEnezi · Site@hotmail.com · 3li.info
Notes: Set the scene: heritage first, life safety first, then technology.

## Slide 3
02 // THE MAP
The numbered map is the digital twin
Smart Souq Al-Mubarakiya · a vision by Ali AlEnezi
67
REGISTRY ENTRIES
9
ZONES
14
SENSOR CLASSES
37
PLACED SENSORS
Every location becomes an ID MUB-Z4-057-WATER-01 is the water quality probe at the fish market, zone Z4.
Every device publishes a signed envelope on mubarakiya/Z4/057/WATER/<device>/telemetry, and the broker rejects unknown devices, which is where zero trust for sensors actually lives.
Ali AlEnezi · Site@hotmail.com · 3li.info
Notes: The map you already have becomes the asset registry: every numbered location is an ID.

## Slide 4
03 // ARCHITECTURE
Four layers, from sensing to decisions
Smart Souq Al-Mubarakiya · a vision by Ali AlEnezi
Sensing
Fourteen classes on private LoRaWAN. Fire, gas, footfall, noise, air, water, cold chain, humidity, waste, tamper, parking, traffic, heat, lighting. Two vendors per class.
Edge
Five gateways, fiber with NB-IoT backup, a redundant edge pair with local rules and 72 hours of autonomy. An OT conduit that passes only signed commands.
Platform
A broker with a certificate per device, time series, a digital twin keyed to the map, a CA that signs firmware. Open source core, with an Azure path.
Applications
A safety first dashboard, alert routing to Kuwait Fire Force with human confirmation, a merchant portal by zone and hour, public wayfinding and open data.
Ali AlEnezi · Site@hotmail.com · 3li.info
Notes: Hardware, data, information, analytics, made concrete. Note the edge: it keeps life safety working offline.

## Slide 5
04 // NETWORK AND EDGE
The edge keeps people safe when the cloud does not
Smart Souq Al-Mubarakiya · a vision by Ali AlEnezi
5 gateways
overlapping LoRaWAN coverage, four on the fiber ring and one on NB-IoT where fiber does not reach
72 hours
store and forward while the platform is unreachable, life safety alerting continues locally
Signed only
the OT conduit accepts commands from an allow list, verified and read back, nothing else
Modes of the edge: connected → degraded, local rules lead → offline, 72 h buffer → recovering, backfill and reconcile. Quarterly drills pull the fiber on purpose to prove it.
LoRaWAN 1.0.4 · MQTT 5 over TLS 1.3 · OPC UA, BACnet, DALI · read only Modbus · syslog and CEF to the SOC
Ali AlEnezi · Site@hotmail.com · 3li.info
Notes: Walk the topology: gateways, backhaul, the municipal edge room, the OT conduit.

## Slide 6
05 // SECURITY
Trust zones and conduits, reviewed before anything is built
Smart Souq Al-Mubarakiya · a vision by Ali AlEnezi
HISN REVIEW
nothing to flag · 6 of 6 IEC 62443 areas
Certificate per device
no shared keys, no default credentials, unknown devices rejected at the broker
Signed commands only
through the OT conduit, second person approval, read back, audited
Humans confirm dispatch
the system raises, a person confirms Kuwait Fire Force, never automation
Ali AlEnezi · Site@hotmail.com · 3li.info
Notes: The blueprint was drawn and reviewed with Hisn. The review caught two real gaps during design.

## Slide 7
06 // SENSORS
Fourteen classes, specified for heat and dust
Smart Souq Al-Mubarakiya · a vision by Ali AlEnezi
FIRE
Heat and smoke
GAS
LPG and CO
FOOT
Footfall, anonymous
HEAT
Heat stress, WBGT
AIR
Dust and air quality
WATER
Water quality
TEMP
Cold chain
HUMID
Humidity
WASTE
Bin fill level
TAMPER
Shutter tamper
PARK
Parking bays
TRAFFIC
Vehicle counts
NOISE
Noise level
LIGHT
Lighting control
Every device: 60 C or better, IP65 minimum, dust tolerant optics, five year battery or mains with backup, neutral enclosures on non historic fixtures. Pilot about 60 devices, full souq about 400, plus parking bays.
Life safety thresholds, examples: heat above 58 C or rising faster than 8 C per minute, LPG above 10 percent of the lower explosive limit, crowd density above 3 people per square meter at an entrance.
Ali AlEnezi · Site@hotmail.com · 3li.info
Notes: Every class open protocol, two qualified vendors, rated for 60 C and IP65 or better.

## Slide 8
07 // A FIRE ALERT, END TO END
From sensor to dispatch in under thirty seconds
Smart Souq Al-Mubarakiya · a vision by Ali AlEnezi
1
Heat spike and smoke at the restaurants area
2
The edge triggers the fire panel and PA locally, within seconds
3
Alert reaches the operations center in under 30 s, crowd density on the map
4
Ops confirms dispatch to Kuwait Fire Force. Automation never dispatches on its own
Then the drill continues: crew on site, LPG valve closed, all clear, and 14 audit events written to the SOC. The site runs this as a playable scenario.
Ali AlEnezi · Site@hotmail.com · 3li.info
Notes: Walk through the sequence. Emphasize local triggering and human confirmation.

## Slide 9
08 // ROADMAP
Five phases, each ending with a decision
Smart Souq Al-Mubarakiya · a vision by Ali AlEnezi
0
Discover and govern
6 to 8 weeks
gate: heritage and privacy approvals
1
Pilot one zone
3 to 4 months
gate: review with merchants and Kuwait Fire Force
2
Scale the souq
6 to 9 months
gate: independent security assessment
3
Intelligence and services
about 6 months
gate: privacy review per data product
4
Operate and replicate
ongoing
gate: yearly review
Phase 1, the pilot: the restaurants street, Safat Square, and Gold Parking. Highest fire and crowd risk, most visible win. Two vendors per sensor class so that interchangeable is proven, not promised.
Most of the money sits in Phase 2 civil works and integration, not in sensors. The pilot is the cheapest way to de risk everything after it.
Ali AlEnezi · Site@hotmail.com · 3li.info
Notes: Gates, not dates. Nothing physical goes live without an independent security assessment.

## Slide 10
09 // WHAT A PILOT WOULD TAKE
An honest picture of a first pilot
Smart Souq Al-Mubarakiya · a vision by Ali AlEnezi
Sensing, about 60 devices
24 heat and smoke under the restaurant awnings
12 LPG and CO in the kitchens
8 anonymous footfall counters
4 noise, 3 air, 2 heat stress
1 water quality probe, 4 waste fill
60 parking bay sensors, 1 traffic counter
6 lighting control nodes
Connectivity and edge
3 outdoor LoRaWAN gateways with battery backup, fiber or NB-IoT backhaul
A redundant pair of fanless edge nodes in a municipal room, an edge firewall pair, and an OT conduit firewall
Neutral, non invasive brackets. Nothing touching historic fabric
Platform and people
The open source platform, sized for the whole souq from day one
A device identity CA, dashboards and alerting, fire panel and PA integration accepted with Kuwait Fire Force
A penetration test and a tabletop exercise before anyone calls it done
Ten percent spares, runbooks, and training
Most of the cost goes into civil works and integration, not into sensors.
Ali AlEnezi · Site@hotmail.com · 3li.info
Notes: Grounded numbers for a first pilot. No prices, it is a vision.

## Slide 11
10 // THE SOUQ
The place we are protecting
Smart Souq Al-Mubarakiya · a vision by Ali AlEnezi
Photographs by Zairon, Diego Delso, and آية سعيد البيطار, Creative Commons via Wikimedia Commons
Ali AlEnezi · Site@hotmail.com · 3li.info
Notes: A pause on the souq itself: the point of all of this.

## Slide 12
This is my dream for Al-Mubarakiya, and I wanted to share it with everyone: that the souq stays as we know and love it, with its soul and its history, and becomes safer through smart technology that works in silence.
A personal vision, shared to read and discuss. The blueprint, the diagrams, the sensor catalog, the registry, the brief, and this deck live on the site.
mubarakiya.3li.info
Ali AlEnezi · 3li.info · linkedin.com/in/alenizi · © 2026, all rights reserved
scan to open
This work is part of an educational experience. The ideas are owned by Ali AlEnezi. The entities mentioned, Kuwait Municipality, the Ministry of Interior, Kuwait Fire Force, NCCAL, CITRA, the Ministry of Electricity and Water, the Ministry of Commerce, the merchants, and SANS, are mentioned only to elaborate on the ideas and have no real link or connection to this work. SANS is named only as a suggestion for training, and none of its copyrighted material is used here. © 2026 Ali AlEnezi. All rights reserved.
Ali AlEnezi · Site@hotmail.com · 3li.info
Notes: Close on the dream again.